## Slide 1: From Onshape to Object
3D printing basics on the Bambu Lab X1-Carbon
ENGR 101 · Engineering Exploration · How Engineers Make Things
Notes: Today's goal: every student leaves knowing the full path from a part in Onshape to a physical object off the X1-Carbon — and why each step matters. Students should have a small part ready in Onshape (or use a provided practice part).

## Slide 2: Warm-up: how was this made?
Pass around a 3D-printed part
Small groups, 5 minutes. Then we share out as a class.
1
Run a fingernail across the surface. What do you feel — and what does it tell you about how it was built?
2
Find the face that was on the build plate. How can you tell?
3
Where would this part break first if you bent it? Why there?
Notes: Let them discover layer lines, the flat 'first layer' face, and that parts tend to split BETWEEN layers. Don't name these yet — collect observations on the board and come back to them on the design-rules slide.

## Slide 3: Three ways to make a part
Subtractive
Start with a block and remove material.
Milling, lathe, laser cutting
Formative
Force material into the shape of a mold or die.
Injection molding, casting, stamping
Additive
Build the part one thin layer at a time.
3D printing (what we're doing today)
Think about it: why would a company 3D print a prototype but injection mold the final product?
Notes: Quick pair-share on the bottom question. Target ideas: 3D printing has no tooling cost and is easy to change (great for 1–10 parts); molding has huge upfront mold cost but each part is cheap and fast (great for 10,000 parts). Connects to the 'manufacture at scale' week.

## Slide 4: How our printer works: FDM
Fused Deposition Modeling — like a very precise robotic hot glue gun
Filament
1.75 mm plastic on a spool
Extruder
Gears push filament forward
Hot end
Melts it (~220 °C for PLA)
Nozzle
0.4 mm opening draws a thin line
Build plate
Heated; part grows layer by layer
Layer height
How thick each layer is
Walls
Solid outer shell lines
Infill
Inside pattern — rarely 100% solid
Supports
Temporary scaffolding for overhangs
Notes: Tie back to the 3D printer disassembly lab — students have already held an extruder and hot end. The four vocab words at the bottom come back when we slice.

## Slide 5: Meet the Bambu Lab X1-Carbon
256 mm
build cube (W × D × H)
0.4 mm
hardened steel nozzle
300 °C
max nozzle temperature
500 mm/s
max toolhead speed
Fully enclosed
Keeps heat steady and fingers out
AMS (Automatic Material System)
Holds up to 4 spools for color/material swaps
Automatic bed leveling
Measures the plate before every print
Micro lidar + AI camera
Inspects the first layer and spots “spaghetti” failures
Notes: Contrast with the Ender 3 if students have seen it: open frame, manual leveling, one filament. The X1-Carbon automates a lot of the calibration — but it can't fix a bad design or bad slicer settings. That's still on us.

## Slide 6: The big picture: six steps
1
Design
Model your part in Onshape
2
Export
Save as STL or 3MF (mm!)
3
Slice
Bambu Studio turns it into layers
4
Send
Send the job to the X1-Carbon
5
Print
Watch the first layer
6
Finish
Remove, clean up, measure
Most failed prints are decided in steps 1–3 — before the printer ever turns on.
Notes: This is the roadmap for the rest of the deck. Each following slide has a gold step tag in the corner so students can track where they are.

## Slide 7: Design for printing
STEP 1 · DESIGN
Big flat face down
A large, flat bottom sticks to the plate and needs no supports.
The 45° rule
Overhangs steeper than ~45° from vertical need supports.
Walls ≥ 0.8 mm
That's two nozzle widths. Thinner walls may not print at all.
Leave clearance
Parts that fit together need a 0.2–0.3 mm gap, or they'll fuse or jam.
Fit the cube
Max 256 × 256 × 256 mm — and smaller prints finish faster.
Details ≥ 1 mm
Tiny text and features smaller than ~1 mm get lost.
Notes: Connect back to the warm-up: the flat face they found = rule 1. Where it broke = between layers (next slide). These numbers are good starting points, not laws — tolerances vary by printer and filament, which is exactly why we measure after printing.

## Slide 8: Which way would you print it?
STEP 1 · DESIGN
L-bracket
Cup
Arch
For each shape, decide as a group: Which face goes on the plate? Will it need supports? If you had to hang weight from it, which orientation would be strongest — and why?
Notes: Small groups → share out. Big insight to let them discover: layers bond weakest to each other, so a part is strongest along its layers and weakest across them. The L-bracket printed standing up (as drawn) may snap at the corner; printed on its side, the layers run around the corner. The cup prints great upright; upside down it needs a full support bed. The arch's top span needs supports or a 'bridge' — or flip it on its side.

## Slide 9: Export from Onshape
STEP 2 · EXPORT
1
Right-click the part
In the Parts list (or right-click the Part Studio tab to export everything)
2
Choose Export…
Opens the export dialog
3
Format: STL or 3MF
Either works with Bambu Studio
4
Units: Millimeter
Bambu Studio expects mm
5
Resolution: Fine
Smoother curves on round features
6
Download the file
Save it somewhere you can find it
STL vs 3MF
STL: just the triangle surface. The universal standard.
3MF: surface plus units, color, and part info in one file.
Check your units!
If a 50 mm part shows up 25× too small or 25× too big, it was exported in the wrong units. (Remember Mars Climate Orbiter?)
Notes: Live demo in Onshape. Export one part at a time to start. The units callout ties back to the communication unit: STL files store numbers with no units attached — the slicer has to guess. 25.4 is the inch-to-mm factor, so an inch/mm mixup shows up as a part 25.4x off.

## Slide 10: What is slicing?
STEP 3 · SLICE
The printer can't read a 3D model. It only follows instructions like “move here, push out this much plastic.”
A slicer is the translator:
3D model your STL / 3MF
Thin layers hundreds of horizontal slices
Toolpaths (G-code) the exact path the nozzle follows
Every layer = one slice
Notes: Our slicer is Bambu Studio (free; installed on lab computers). A 30 mm tall part at 0.2 mm layers = 150 layers. Ask: what happens to print time if we halve the layer height?

## Slide 11: Slicing in Bambu Studio
STEP 3 · SLICE
1
Open the Prepare tab
This is where you set up the plate
2
Printer: Bambu Lab X1 Carbon 0.4 nozzle
Top-left printer dropdown
3
Plate type
Match the plate actually in the printer
4
Filament
Match the spool & AMS slot (e.g., Bambu PLA Basic)
5
Import your file
Drag it in, or Ctrl+I
6
Orient it
Lay on Face (F) — click your big flat face
7
Check settings
Layer height, walls, infill, supports (next slide)
8
Click Slice plate
Then review the Preview tab
Notes: Demo on the projector, then have students follow along with their own part. Most common mistakes: wrong printer profile, plate type mismatch (prints don't stick or the printer warns you), and forgetting to orient. If the part comes in way too small/large, go back to export units.

## Slide 12: The settings that matter most
STEP 3 · SLICE
Setting | What it controls | Start with | Change it when…
Layer height | Detail vs. speed | 0.20 mm (Standard) | 0.12 for fine detail; 0.28 for a fast draft
Wall loops | Strength of the outer shell | 2 | 3–4 for parts that get loaded or screwed into
Sparse infill | How full the inside is | 15% | 25–40% for strong parts; 10% for display models
Supports | Scaffolding under overhangs | Off | Turn on (tree, auto) for overhangs past ~45°
Brim | Extra first-layer border | Auto | Tall or tiny-footprint parts that might tip or lift
Change one setting at a time and watch what happens to print time and filament in the preview.
Notes: Infill and walls are in the Strength tab; supports in the Support tab; brim in Others. Mini-experiment: have each group slice the same part at 10% vs 40% infill and compare time and grams. Most strength comes from walls, not infill — a fun surprise for students.

## Slide 13: Read the preview before you print
STEP 3 · SLICE
Print time
Will it finish before class ends?
Filament (g)
Less plastic = less waste, less cost
Drag the layer slider and check:
Layer 1 has lots of solid contact with the plate
Nothing is printing in mid-air with nothing below it
Supports are only where you expect them
Holes and small features actually show up
Only one copy of your part is on the plate
Notes: Too long? Try 0.28 mm layers, lower infill, or scale the part down. Instructor sign-off on the preview before sending is a good checkpoint to catch issues early.

## Slide 14: Send it to the printer
STEP 4 · SEND
Click Print plate, choose our X1-Carbon, then check these boxes:
Bed leveling
Printer scans the plate first
Flow dynamics calibration
Tunes extrusion for this filament
Use AMS
Pulls filament from the slot you chose
Timelapse (optional)
Fun to watch — and great for spotting failures
Then click Send. The printer heats up, levels the bed, and calibrates before plastic comes out — the first few minutes look like nothing is happening. That's normal. No network? Export the sliced file to a microSD card instead.
Notes: Adjust to our lab setup: who sends jobs (students vs. instructor), cloud vs. LAN vs. microSD, and how the queue works. Also note whether the printer is bound to a shared lab Bambu account.

## Slide 15: Before you walk away
STEP 5 · PRINT
Pre-print checklist
Build plate is clean — no fingerprints or leftover plastic
The plate in the printer matches the plate in Bambu Studio
The right filament is loaded in the AMS slot you chose
Nothing loose inside the chamber
Watch the first layer
Most failures happen here. Lines should be flat, slightly squished, and touching each other. If it's lifting, curling, or dragging around — stop the print and ask for help. The AI camera also watches, but your eyes are faster.
Notes: Oils from fingers are the #1 cause of prints not sticking. Handle the plate by the edges; wash with dish soap and water if needed.

## Slide 16: After the print
STEP 6 · FINISH
Let it cool
Parts pop off easier once the plate cools
Flex the plate
Remove it and bend gently — the part releases
Remove supports
Pliers + safety glasses; pull away from you
Reset the printer
Clear scraps, put the plate back in
Measure it
Calipers vs. your Onshape dimensions
Your print is data. Did the holes come out smaller than designed? That's a tolerance lesson — not a failure.
Notes: Measuring closes the loop: holes almost always print a bit small and outside dimensions a bit large. Have students record designed vs. measured for 2–3 features.

## Slide 17: When things go wrong
What you see | Likely cause | Try this
Part won't stick / corners lift | Dirty plate or too little contact | Wash plate; add a brim; bigger flat face down
“Spaghetti” — tangled mess | Part came loose or printed in mid-air | Check orientation and supports in preview
Holes or slots too tight | No clearance for the printer's tolerance | Add 0.2–0.3 mm in Onshape and reprint
Supports won't come off | Supports touching too much of the part | Reorient to need fewer supports; use tree supports
Part snapped along a layer | Load pulled the layers apart | Rotate so layers run along the load; add walls
Notes: Keep a 'failure wall' or bin of failed prints — they make great teaching examples and reinforce that iteration is normal.

## Slide 18: Lab safety & norms
It's hot
Nozzle up to 300 °C, plate over 100 °C. Don't touch either.
Door stays closed
Don't open the door or reach in while it's printing.
Hands off controls
Ask before changing filament, settings, or canceling someone's print.
Eyes protected
Wear safety glasses when cutting or snapping off supports.
Log your print
Name, part, time, and how it turned out.
Report problems
Weird noises, smells, or errors? Tell the instructor right away.
Notes: Edit the log item to match our actual print log (paper sheet, Google Form, etc.).

## Slide 19
Engineers iterate
Design
Print
Measure
Redesign
Exit ticket
Name one dimension where your print didn't match your Onshape model. By how much, and why do you think?
Which slicer setting would you change on your next print — and what do you expect to happen?
What's one thing you'd tell a classmate before their first print?
Notes: The prompts ask for a specific dimension and a specific prediction to push past generic answers. Optional extension: redesign with corrected tolerances and reprint next session.